Reprapboard OVERVIEW

# Design goals for reprapboard

## Main goals:
- Stable solution
- affordable components
- includes all needed components to fully controll a reprap printer
- support for heated bed controll
- support for heated chamber control
- support for two extruders
- support for voltages up to at least 24V
- resettable fuses for main components, replaceable fuses for high power components
- support for thermistor and thermocouple for the two extruders
- native USB support
- 1/16 microstepping or better for X,Y,Z
- 1/8 microstepping or better for extruders
- complete documentation
- compatibillity with mainstram firmware where possible
- Distinct power paths for stepperdrivers, heater mosfets, logic components
- components readily available
- Two layer PCB
- I2C
- RS485
- sd-card reader
- display
- keypad
## Optional goals:
microstepping can be changed in firmware
# Components
This section lists hardware candidates for the BOM and their upsides/downsides
## MCU
### Atmel AT90USB1286
+includes USB Support
## Stepper drivers for X,Y,Z

### TI DRV8824
+1/32 microstepping
-1,6A max
### TI DRV8825
+1/32 microstepping
+2,5A
+pin compatible with drv8824
-not yet available
-more expensive
## Stepper Drivers for E0 E1
### TI DRV8811
+2,5A
-1/8 microstepping only
### TI DRV8824
+1/32 microstepping
-1,6A max
### TI DRV8825
+1/32 microstepping
+pin compatible with drv8824
-not yet available
-more expensive